## Slide 1
ME 3310 — Mechanics of Materials
Lecture 9: Beam Bending & Deflection — my notes
Marcus Reyes · Mechanical Engineering, Year 3

## Slide 2
Euler–Bernoulli beam theory
What the formulas on the next slides assume
• Plane sections stay plane and perpendicular to the neutral axis
• Small deflections and slopes; linear-elastic material (Hooke's law)
• Governing equation: E I · d²v/dx² = M(x)
• Integrate twice, then fix the constants with boundary conditions:
– pinned / roller support: v = 0
– fixed (built-in) support: v = 0 AND dv/dx = 0
– symmetry about midspan: dv/dx = 0 at x = L/2

## Slide 3
Bending stress
Normal stress from the internal bending moment
σ(y) = − M y / I
Maximum at the outer fibre, y = c: σ_max = M c / I = M / S
Section modulus: S = I / c
Tension on one side of the neutral axis, compression on the other; σ = 0 on the axis.
Design check: σ_max ≤ σ_allow = σ_yield / FS

## Slide 4
Case A — simply supported, point load at midspan
P
L
Reactions: R_A = R_B = P / 2
M_max = P L / 4 (at midspan)
δ_max = P L³ / (48 E I) (at x = L/2)
Slope at the supports: θ = P L² / (16 E I)

## Slide 5
Case B — cantilever, point load at the tip
P
L
Reaction moment at the wall: M_wall = P L
M_max = P L (at the fixed end)
δ_max = P L³ / (3 E I) (at the tip)
Slope at the tip: θ = P L² / (2 E I)

## Slide 6
Worked example — Case A
Steel W-section: L = 3.0 m, P = 12 kN, E = 200 GPa, I = 8.0×10⁻⁶ m⁴, c = 0.10 m
M_max = P L / 4 = (12 000 N)(3.0 m) / 4 = 9.0 kN·m
σ_max = M c / I = (9 000)(0.10) / (8.0×10⁻⁶) = 112.5 MPa
δ_max = P L³ / (48 E I) = (12 000)(27) / (48 · 200×10⁹ · 8.0×10⁻⁶) = 4.22 mm
Checks: δ ≤ L/360 = 8.33 mm ✓ σ ≤ 250 / 1.5 = 166.7 MPa ✓

## Slide 7
Worked example — Case B (same beam, cantilever)
Same L, P, E, I, c
M_max = P L = 36 kN·m
σ_max = M c / I = (36 000)(0.10) / (8.0×10⁻⁶) = 450 MPa ✗ (yield is only 250 MPa)
δ_max = P L³ / (3 E I) = (12 000)(27) / (3 · 200×10⁹ · 8.0×10⁻⁶) = 67.5 mm ✗ (limit 8.33 mm)
Cantilever vs simply supported: moment 4× larger, deflection 16× larger

## Slide 8
Open question (mine)
Why is the cantilever exactly 16× worse in deflection but only 4× worse in moment?
I can recite both formulas — I want to be able to explain the factor from the
boundary conditions, not from the table.

## Slide 9
Homework 9 — Problem 4 (not started)
A simply supported steel beam, L = 4.5 m, carries a central point load P.
E = 200 GPa, I = 12×10⁻⁶ m⁴, c = 0.12 m, σ_yield = 250 MPa, FS = 1.5.
Deflection limit: δ_max ≤ L / 360.
Find the largest P the beam can carry, and state which check governs.